## Slide 1
Project Name
USB Mobile Charger
Presented By |  | 
Sujit Debnath | Abdullah Al Mamun | Mustafizur Rahman

## Slide 2
Project Objectives
This project is all about a cell phone charger.
It can charge any kind of mobile handset.

## Slide 3
Project Distribution
Step down AC voltage
Rectification
Filtration
Voltage Regulation
Mobile phones generally charge with 5V regulated DC supply.
We had to build a 5V regulated DC supply from AC supply which is 220V, since we used home electricity line.
For the implementation of this project, we had to divide the work process in four steps. Such as,

## Slide 4
Filter
Voltage Regulator
Out-
put
Diode
Rectifier
Transformer
AC
Source
Block Diagram of the Project
220V-240V AC signal
Convert 220V to 12V
AC signal
Convert AC
to DC
Generated proper
DC signal
Regulate 5V
Mobile
handset

## Slide 5
Equipment's
Component Details | Specification
Step down Transformer | 12Volt 3A
p-n Junction silicon diode | 1N4007
Capacitor | 0.01µF
 | 1000 µF 25V
Voltage Regulator | LM7805
Breadboard | -
Plug, wires & data cable | -

## Slide 6
AC Signal
220V – 240V
Transformer
D1
D2
D3
D4
C1
1000µF
C2
0.01µF
VI
VO
GND
LM7805
Output
Circuit Diagram

## Slide 7
Difficulties Faces
We faced our first difficulties when we tried to put the AC signal on breadboard as an input. Since we didn’t have any signal generator, we had to use the home electricity line. That’s why, we brought the plug, wires and connected them together. Finally, we set that input line with transformer and breadboard.
Another simple difficulty was with the USB type A connector. This connector couldn’t set on breadboard for its weird pin head. To solve this issue, we had to cut a data cable and connect it to the breadboard.

## Slide 8
Future Recommendations
This mobile charger circuit can be modified in such a way that it can charge more than one device at the same time.
It can also be modified such that it can do multiple tasks. Such as, it can charge mobile device and run a motor parallel to each other.

## Slide 9
Thank You Everyone!
ANY
QUERIES?